## Slide 1: Embedded Microcomputer Implementation for an IoT Gateway
Seminar Presentation
Raspberry Pi 5 IIoT Gateway + Pico W Sensor + PLC Integration

## Slide 2: Agenda
Project motivation and objectives
System architecture and data flow
Hardware and software stack
Key implementation features
Deployment, testing, and results
Challenges, future improvements, and conclusion

## Slide 3: Problem Statement & Motivation
Industrial systems require interoperability between OT devices and IT analytics platforms.
Legacy PLC systems must work with modern wireless sensing and real-time monitoring.
Target: build a practical, low-cost gateway bridging MQTT, OPC UA, and visualization.

## Slide 4: Project Objectives
Implement IIoT gateway on Raspberry Pi 5 for process control workflows.
Integrate Raspberry Pi Pico W sensor nodes with MQTT telemetry.
Connect Siemens S7-1500 PLC via OPC UA client.
Expose MQTT telemetry as OPC UA variables for interoperability.
Store historical data in PostgreSQL and visualize in Grafana.
Provide web-based configuration and diagnostics.

## Slide 5: System Architecture
Pico W (MQTT) → Gateway → OPC UA Server exposure + Database storage
Siemens S7-1500 (OPC UA) → Gateway OPC UA Client → Database
PostgreSQL → Grafana dashboards + Flask Web UI
Gateway acts as protocol bridge, data processor, and control point

## Slide 6: Hardware Components
Raspberry Pi 5: central gateway hardware
Raspberry Pi Pico W: Wi-Fi edge sensor node (DHT22 + OLED)
Siemens S7-1500 PLC: industrial control data source
Network services: Mosquitto broker, PostgreSQL, Grafana

## Slide 7: Gateway Software Stack
Flask app with REST API and real-time dashboard
MQTT service: topic subscriptions and data ingestion
OPC UA server service: expose selected MQTT variables
OPC UA client service: browse/read PLC variables
Database service: persistence for telemetry and configuration

## Slide 8: Pico W Sensor Node Capabilities
DHT22 temperature/humidity acquisition
MQTT publishing via lwIP MQTT implementation
OLED status display (SSD1306)
Local web dashboard and JSON API
Flash-persistent config and setup AP mode

## Slide 9: Key Features Delivered
MQTT-to-OPC UA bridge for protocol interoperability
Web UI for variable browsing and configuration
Real-time status monitoring for MQTT/OPC UA/Database
Historical data analysis with Grafana integration
Operational troubleshooting guides and structured logging

## Slide 10: Deployment & Validation
Platform: Raspberry Pi OS + Python 3.9+ + Mosquitto + PostgreSQL + Grafana
Deployment via virtual environment and requirements-based setup
Production startup supported through systemd service
Validation focus: connectivity, API behavior, data persistence, UI correctness

## Slide 11: Challenges and Solutions
Challenge: integrating heterogeneous protocols (MQTT and OPC UA)
  Solution: dedicated gateway bridge architecture
Challenge: maintaining visibility and diagnostics
  Solution: unified dashboard, API status endpoints, and logs
Challenge: robust edge deployment behavior
  Solution: persistent configuration and guided troubleshooting

## Slide 12: Future Improvements
Security hardening with authentication and TLS end-to-end
Additional protocol and sensor support
Edge analytics/anomaly detection at gateway layer
Alerting and notification workflows
Containerized deployment and CI/CD automation

## Slide 13: Conclusion
Project demonstrates a practical IIoT gateway for process-control integration.
Successfully bridges wireless sensing, PLC data, and monitoring platforms.
Architecture is modular and suitable for pilot-to-production growth.
Thank you — Questions?